## Slide 1: Spatiotemporal Data Management and Analytics An Introduction to Spatial Databases
By Prof Xiaofang Zhou, Dr Lei Li and Dr Pingfu Chao
The University of Queensland

## Slide 2: Learning Modules
 | Date | Lecture | Lecturer
1 | 22/6 | Course Introduction and RDBMS Review | Prof Xiaofang Zhou
2 | 22/6 | Introduction to Spatial Databases | 
3 | 23/6 | Spatial Data Organisation | Dr Lei Li
4 | 23/6 | Spatial Query Processing | 
5 | 24/6 | Managing Spatiotemporal Data | Dr Pingfu Chao
6 | 24/6 | Managing High Dimensional Data | Dr Lei Li
 | 25/6 | 端午节 | 
7 | 26/6 | Advanced Topic: Route Planning in Road Networks | Dr Lei Li
8 | 26/6 | Future Trends, Course Review and Discussions | All
 |  | Revision Period | 
 | 9 July | Final Report Due | 

## Slide 3: Learning Objectives
What we will cover
  Spatial Data Types and Modelling
  Spatial Relationships, Operations and Queries
  SDBMS Architectures
Goals
  Understand how spatial data is different from the relational data
  Understand how these differences affect those relational techniques we learned before
  Understand what spatial DBMS is

## Slide 4: Readings
R. Güting, An Introduction to Spatial Database Systems, The VLDB Journal, 3:4, 1994
Hanan Samet and Walid G. Aref, Spatial Data Models and Query Processing, in W. Kim (Ed), Modern Database Systems: The Object Model, Interoperability, and Beyond, 1995
…all papers are provided

## Slide 5: Why Spatial DBMS?
Huge amounts of spatial data, extensive and comprehensive
  Google Map: 20 Petabytes of data in 2012
    Nowadays: every phone that enables traffic condition sharing…
  Uber/DiDi: Terabytes of taxi trajectory per day
  OpenStreetMap: Planet.osm 1166 GB for the static Earth
    NearMap
  NASA satellites image: TB per day
  Twitter / Weibo with geo-tags
  Weather / Climate Data: windy.com, every 6 hours
  Foursquare check-in: 3 billion visits / month in 2017
  Cellular signalling data from Vodafone / Telstra…
  …

## Slide 6: Why Spatial DBMS?
Increasing needs to store, search and use spatial data, together with other data, efficiently, enterprise-wide
  File system-based solutions are not good enough
    Hard to manage, search, share,…
  Application-based solutions are not good enough either
    Hard to share
    It is essentially a common data and operation
    Push the common operations push down
  The same reason for RDMBS

## Slide 7: Why Spatial DBMS?
RDBMS cannot support spatial data directly
  Store the spatial objects into tables?
  How about spatial operations?
    Find the fuel prices of all petrol stations with 5km of my current location
    List of the suburbs along Brisbane river
    What is the average speed of M3 from Kangaroo Point to Milton during last 10 minutes?
  How to retrieve the spatial data efficiently?
    Hash?
    B-Tree?

## Slide 8: Spatial Data
Any data with a location component
  2D Space
    Geographical space: GIS, Urban Planning
    Graphics: CAD, VLSI Design
  3D Space
    : The universe, brain model, molecule structure…
    : Trajectory
Two types of spatial data
  Those data about the space (e.g., road networks, maps)
  Those data about objects (e.g., location of shops, location about cars)

## Slide 9: More Spatial Data
Natural Area Data
  Soil types, land use (industrial, agriculture, zoning etc), vegetation, water (rivers, ponds etc)
Manmade Area Data
  Political and administrative boundaries, school districts, emergency service areas, land records data (lot boundaries, zoning, easements)
Network Data
  Utilities (phones, sewers, water, electricity etc)
  Roads (centrelines, curb lines, intersections, lights)

## Slide 10: Modelling Spatial Data

## Slide 11: Vector Data
A spatial object is described by a sequence of points
  Defined using geometric data types
    Points, Lines and Polygons / Region
  Work with coordinates
Advantages
  Suitable for processing & manipulation
  More compact, better rendering quality
  Query by spatial relationships
Disadvantages
  Continuous data is poorly stored and displayed

## Slide 12: Raster Data
A spatial object is described by a set of pixels
  E.g., satellite imagery, remote sensing
  Work with pixels
Advantages
  Suitable for display
  Query by colour, texture, etc.
  Efficient for some type of processing
    Continuous information like
      Temperature / Elevation / Humidity
      Census / Health / Employment
    Map Algebra[1]
Disadvantages
  Pixelated look
  Hard to display linear features and paths
  Hard to perform topology rules
  Large data size

## Slide 13: Vector vs Raster Data
Different representation of same data
Suitability application-dependent
Mutually convertible
  Rasterization
  Vectorization
Often used together
  E.g., overlay satellite image, road network, elevation data etc.
  Hybrid mode for Google Earth / Google Map
We deal with the vector data in spatial databases

## Slide 14: Coordinate Systems
Assigning coordinates to uniquely identify a location
Establishing relationships between sets of such coordinates
Cartesian Coordinates
Local Coordinates
  Cartesian coordinates in a non-Earth (non-georeferenced) coordinate system, like CAD applications and local survey

## Slide 15: Geographical Coordinate Systems
Map Projection
  Creating a 2D representation of a 3D earth model
  Commonly used map projections
    Mercator
    Developed by Gerhardus Mercator, a Flemish Cartographer, in 1569, and the flat map of the world in UTM are found in every school class room

## Slide 16: Geographical Coordinate Systems
Map Projection
    UTM (Universal Transverse Mercator)
      Cartesian Coordinate
      60 Zones, each 6 degree of longitude
      Unit in meter

## Slide 17: Geographical Coordinate Systems
Map Projection
    UTM (Universal Transverse Mercator)
      Badly distorts Greenland, Alaska, and Australia.
    AMG (Australian Map Grid)
    UPS (Universal Polar Stereographic)

## Slide 18: Geographical Coordinate Systems
Lat/long system measures angles on spherical surfaces
    Lat/long values are NOT Cartesian (X, Y) coordinates
      1° of longitude at the equator  1° of longitude near the poles
      1°
Spatial data (and metadata) standard to record mapping parameters used
  Spatial data must be aligned before they can be used together

## Slide 19: Spatial Data Acquisition
There are many publically available spatial datasets
  Government sources, and other providers such as Google
    http://www.spatial-data.brisbane.qld.gov.au
  Open Street Map / Near Map
  Mash-up can be used
  Meta-data is important, and so is data provenance
Generating new data
  Remote sensing
  Field data
    Survey data
    GPS devices
  Crowd Sourcing

## Slide 20: Remote Sensing
camera
Plane of photograph
Ground plane
A
B
D
C
Change of scale

## Slide 21: Spatial Data Accuracy
Accuracy – how accurate is the data (i.e., how close the recorded location of a spatial feature is to its ground location)
  Scale: the ratio between distance on a map and the corresponding distance on the earth
    Scale is 1:10,000, meaning that 1 unit of measurement on the map represents 10,000 of the same units on the earth's surface
  Resolution: the size of the smallest feature that can be represented in a surface
    When scale decreases, resolution decreases too
  Precision: how exactly the location is recorded (i.e., # of digits)
Errors can be introduced from many sources, from data capturing, data editing and data simplification, and data processing operations

## Slide 22: Spatial DBMS
A spatial database system is a database system
  Without non-spatial data, spatial data is meaningless in real-life
It offers spatial data types in its data model and the query language
It supports spatial data types in its implementation, providing at least spatial indexing and efficient algorithms for spatial join queries and other types of queries
  Retrieve the data without scanning the whole set
  Join the objects without full cartesian product

## Slide 23: Alternative Names
AM/FM System (80s)
  Automated Mapping and Facilities Management
  Associated with public utilities like gas, electric, water and telecommunications
GIS (Geographical Information System)
Pictorial (or Image) Database Systems
  Remote sensing by satellite, computer tomography in medical
Land Information Systems
Natural Resources Information Systems
Spatial Data Management (or Handling) System
Object-Relational Database Systems
  Oracle has many types of data cartridges, including one for spatial data
  New data types, procedures, indexes, queries,…
  Spatial, Text, Image, Time series

## Slide 24: GIS and Spatial Databases
GIS Applications
  Front End
  Data capture, editing, conversion, conflation
  Map generation
  Image processing
  Data analysis (in application areas)
  Use both raster and vector
Spatial DBMS
  Back End
  Integrated management of spatial and non-spatial data
  Database support expected in a RDBMS, independent from applications
  RDBMS-comparable performance

## Slide 25: SDBMS is a Multidiscipline Area
Cartography
  Display of visual information (or, you can call it visualization)
Computer Science
  Databases, Computer Graphics, Image Processing, Machine Learning
Geography
  Spatial Analysis
Mathematics
  Geometry, Graph Theory
Statistics
  Models, Analysis of error
Photogrammetry, remote sensing, surveying…

## Slide 26: History
London 1854, Dr John Snow
  The father of epidemiology
  Paper Mapping Analysis with Cholera Clusters
  Illustrate how cases of cholera were centered around a water pump
    City layer, Water pump layer, Cholera cluster layer,…
  The beginning of spatial analysis

## Slide 27: History
Canada: Geographic Information System (60s)
  Manual analysis was almost as costly as the surveys
    Produced maps which indicated the capability of land to sustain agriculture, forestry, recreation and wildlife
  Assisted in the development of regulatory procedures for land-use management and resource monitoring
  Overlay, Measurement, and Digitizing/Scanning.

## Slide 28: History
American Bureau of Census
  1970 census (Only urban areas)
    Digital input of the 1970 Census
    GBF-DIME (Geographic Base File – Dual Independent Map Encoding)
    Digitize Census boundaries, roads and urban areas
      Intersections, streets, and blocks became analogous to points, lines, and polygons
      Street address & UTM coordinate
      Topology + Direction
  TIGER (Entire country, 1990 census)
    Topologically Integrated Geographic Encoding and Referencing system

## Slide 29: History
ODYSSEY project (the 70’s)
  Harvard Laboratory for Computer Graphics and Spatial Analysis
  SYMAP: Vector models, mapping on a line printer
  ESRI: Arc/Info
    Environmental Systems Research Institute

## Slide 30: History
Australia
  From CSIRO: SIRO-DBMS (SDM) (in the late 80’s)
  Many small GIS companies
Main-stream DB vendors (late 1990’s)
  Oracle, Informix, IBM (DB2), Microsoft (MapPoint)
And for the last ten years, Google and many Internet companies…

## Slide 31: Spatial Data Models
Objects in space (Object-based)
  Single objects
    Point (User, City, POI)
    Line / Polyline (River, Cable, Road)
    Polygon or Region (Forest, Lake, City)
  Spatially related collections of objects
    Partition (Land use, districts, land ownership)
    Network (Roads, rivers, electricity, phone)
Pine
Oak
Fir
0
2
4
2
4
Area-ID | Dominant Tree | Area
FS1 | Pine | [(0,2), (4,2), (4,4), (0,4)]
FS2 | Fir | [(0,0), (2,0), (2,2), (0,2)]
FS3 | Oak | [(2,0), (4,0), (4,2), (2,2)]

## Slide 32: Spatial Data Models
Space itself (Field-based)
  The spatial extent, Euclidian space or other types of spaces (frame/location references, dimension#, distance measures)
    Framework: The space, coordinate, and partition
    Field Function: Maps each partition to its attribute value
    Field Operation: Addition, Composition
      Local, Focal, Zonal
  More related to the raster image
Pine
Oak
Fir
0
2
4
2
4

## Slide 33: The Underlying Space
Euclidean space is continuous real number
  Computer numbers are finite and discrete, with limited approximation
Problems: numerical rounding errors and topological inconsistency and degeneracy
Is D on A?
Is D contained in the area below A & B?
A practical solution: for two points a and b, never ask if a=b; instead, test if distance(a, b) < ε

## Slide 34: Geometry in Data Model
To represent real-world spatial objects using database objects (based on the data model)
  Create a table to store the land use information
Relational data model
  BLOB
    Binary Large OBject
      “The thing that ate Cincinnati, Cleveland, or whatever”
    landuse(area: BLOB, type: string)
      Not searchable, Cannot be indexed, No operation…

## Slide 35: Geometry in Data Model
To represent real-world spatial objects using database objects (based on the data model)
  Create a table to store the land use information
Relational data model
  Table
    landuse(areaID: number, type: string);
    polygon(areaID: number, pntID: number, x: number, y: number)
Area-ID | Dominant Tree
FS1 | Pine
FS2 | Fir
FS3 | Oak
Area-ID | pntID | x | y
FS1 | 0 | 0 | 2
FS1 | 1 | 4 | 2
FS1 | 2 | 4 | 4
FS1 | 3 | 0 | 4
… | … | … | …

## Slide 36: Geometry in Data Model
To represent real-world spatial objects using database objects (based on the data model)
  Create a table to store the land use information
Spatial Data Model
  landuse(area: polygon, type: string)
  Data Type
    Valid Values
    Supported Operations

## Slide 37: Spatial Data Model in Oracle
Element, Geometry and Layer
Element: the basic building block of a geometric feature
  Point data: One point, stored as an pair
  Line data: Two points representing the start and the end of a line segment
  Polygon data: A sequence of coordinates, one vertex pair for each line segment of the polygon
    Both boundary and the interior (pizza and doughnut)
      Counter-clockwise for exterior
      Clockwise for interior
    Complex polygons
      Self-intersecting boundary
      Multiple dis-connected components
      Zero or more interior rings (holes)

## Slide 38: Spatial Data Model in Oracle
Geometry: representation of a user’s spatial feature, modelled as an ordered set of elements
  Each geometry has a unique ID, and can be associated with a set of attributes
  A geometry might describe a lake
    A polygon with nested polygons for islands
    Attributes such as lake name, water capacity, fauna, flora, …

## Slide 39: Spatial Data Model in Oracle
Layer: a collection of geometries having the same attribute set
  Examples: soil types, road network, political boundaries, population density, crops, weather conditions,…
Transport Noise Corridor Overlay
Koala Habitat Areas
Magpie Swooping

## Slide 40: Data Model in DB2
Multipolygon
Multi-linestring
Linestring
Multipoint
Point
polygon
Rectangle
Square
Ellipse
Circle

## Slide 41: Data Model in PostGIS
  Spatial data types are organized in a type hierarchy
  Each sub-type inherits the structure (attributes) and the behaviour (methods or functions) of its super-type.

## Slide 42: Spatial Relationships
Topological
  E.g., inside, intersect, adjacent
  Invariant under translation such as rotation and scaling
Directional
  E.g., above, left, north of
  May change with rotation
Metric
  E.g., distance
  May change with scaling

## Slide 43: Defining Spatial Relationship
Q: How to define a spatial relationship precisely?

## Slide 44: Formal Definitions
Better understanding of the complex semantics of spatial objects and operations at the designer's level
Clarity and consistency at the user’s level
A step towards standardization
Relational Operation ?

## Slide 45: The 9-Intersection Matrix
Ab: boundary
Ai: interior
Ae: exterior
Egenhofer, M.J.; Herring, J.R. (1990). "A Mathematical Framework for the Definition of Topological Relationships"

## Slide 46: The 8 Spatial Relationships (I)
Complete, and Mutually Exclusive.
disjoint
meet
cover
covered_by
overlap
contain
inside
equal
A
B
A
A
A
A
A
A
A
B
B
B
B
B
B
B

## Slide 47: The 8 Spatial Relationships (I)
disjoint
contain
inside
equal
A
B
A
A
A
B
B
B
disjoint
contain
inside
equal

## Slide 48: The 8 Spatial Relationships (I)
meet
cover
covered_by
overlap
A
A
A
A
B
B
B
B
cover
covered_by
overlap
meet

## Slide 49: Operations for Spatial Queries
Basic Spatial Operations
  Selection, Projection, Amalgamation
  Containment, Region, Intersection, Overlay, Fusion, Windowing, Clipping, Centre, Boundary
  Area, Perimeter, Distance
Other Spatial Operations
  Nearest Neighbours, Similarity Search, Skyline Queries
Complex Spatial Queries
  Multiple predicates/operations, spatial sub-queries

## Slide 50: Projection Query
corn district 1
corn district 2
wheat district 4
wheat district 3
district 1
district 2
district 4
district 3

## Slide 51: Selection Query
corn district 1
corn district 2
wheat district 4
wheat district 3
wheat district 4
wheat district 3

## Slide 52: Containment Query
  Given a spatial object O, find all objects in the map that completely contain O.
  When O is a point, the query is called Point Query
O
O
O is a polygon (O is the green one) and the red one is the query result.
O is a point (the green dot).

## Slide 53: Region Query
  Given a region R, find all objects in the map that intersect R
  When R is a rectangle, the query is called Window Query
R
R

## Slide 54: Overlapping Query
corn district 1
corn district 2
wheat district 4
wheat district 3
corn district 1
corn district 2
wheat district 4

## Slide 55: Clipping Query
corn district 1
corn district 2
wheat district 4
wheat district 3
corn
wheat
corn

## Slide 56: Fusion/Amalgamation Query
corn district 1
corn district 2
wheat district 4
wheat district 3
corn
wheat
…important applications in spatial OLAP and spatial data mining
Notes: Rainfall

## Slide 57: Overlay Query
corn
vegetable
grass
wheat
soil1
soil2
soil3
soil4
Wheat/soil1

## Slide 58: Spatial Query Language
  CREATE TABLE ROADS
    (Road_id NUMBER,
    Road_name CHAR(30),
    Road_type CHAR(30),
    Route LINE_SEGMENT);
  CREATE TABLE REGIONS
    (Region_id NUMBER,
    Region_name CHAR(30),
    Region_zip NUMBER,
    Region_Type CHAR(30),
    Location POLYGON);

## Slide 59: Denoting SDT Values Input
    SELECT Expression
    FROM Table
    WHERE Conditions
Expression
  Column, Aggregation Function, Operations,…
Conditions
  Column1 Column2 / Constant
How about Spatial Query?

## Slide 60: Denoting SDT Values Input
Problem: “Brisbane” vs. the geometry of Brisbane
Define named atomic data type values
    DEFINE Brisbane
    ELEMENT SELECT boundary
    FROM city // city(name, boundary, ...)
    WHERE name = “Brisbane”;
Use spatial constants
    WHERE boundary inside POLYGON(100, 102.3; 1.5, 107; ….);

## Slide 61: Fundamental DB Operations (I)
Selection
    SELECT *
    FROM river // river(name, route, …)
    WHERE route intersect PacificHighway;
Join
    SELECT river.name, road.name
    FROM river, road // road(name, route, …)
    WHERE river.route intersect road.route;

## Slide 62: Fundamental DB Operations (II)
Function applications
    SELECT river.name, road.name,
    intersection(river.route, road.route)
    FROM river, road
    WHERE river.route intersect road.route;
    SELECT river.name,
    length(intersection(river.route, Queensland))
    FROM river
    WHERE river.route intersect Queensland;

## Slide 63: Fundamental DB Operations (III)
Other set operations
    SELECT fusion(area), round(amount/100)*100
    FROM rainfall //rainfall(area, date, amount)
    WHERE date = ‘12/1/2011’
    GROUP BY round(amount/100);

## Slide 64: SDBMS Architectures
Requirements
  Representations for spatial data types
  Procedures for spatial operations, including spatial join algorithms
  Spatial index structures, and access operations
  Spatial query optimizer with cost functions & statistics
  Spatial query language, incorporating spatial data types, operations and graphical I/O
Three generations
  Using file systems; using standard RDBMS; integrated systems

## Slide 65: 1st Generation: Using File System
Problems:
No high level data definition
No flexible querying
No DBMS support (eg, TM)
Spatial data stored in file system
Proprietary GIS API
Proprietary GIS API
File System
GIS Data
Engine
Geometry, indexes, and attributes
GIS Tools

## Slide 66: 2nd Generation: Using RDBMS (I)
Dual Architecture:
Easy implementation
Efficient for spatial or aspatial queries
But not both!
Spatial data stored in a GIS system
Proprietary GIS API
Proprietary GIS API
Spatial
Subsystem
Integration
Layer
Standard
RDBMS
SQL
Aspatial data stored in a RDBMS
GIS Tools
Geometry, indexes
Attributes

## Slide 67: 2nd Generation: Using RDBMS (II)
SQL
GIS Data
Engine
Standard
RDBMS
Layered Architecture:
Representing SDT as a set of tuples, one tuple per point or line segment; or as long fields (ie, uninterpreted byte strings).
Mapping SDT into numbers and using B-Tree as index.
Right step towards integrated system
Poor spatial performance.
GIS Tools
SQL

## Slide 68: 3rd Generation: Part of ORDBMS
Spatial data stored as User Defined Data Types in DBMS with other data
SQL
Integrated architecture:
Future direction
Possibility for users to extend the system
Now a mature technology
Performance still a problem for for complex queries
Transaction Management is hard (for long running transactions)
ORDBMS
GIS Tools

## Slide 69: SDBMS Implementation
Continues space vs Discrete computer numbers
High level query language (eg, SQL-like)
Spatial query processing (at least spatial join)
Spatial data access methods (indexing)
Other DBMS issues
  Query optimization
  Transaction management
  Integrity and consistency
  Parallel processing
  Spatial data warehousing and data mining

## Slide 70: Summary
Spatial DBMS is still a DBMS
  Data types and query languages may look different, but are still the same in essence
  Just need to think data types in its intrinsic meaning
If your job is to develop a database system to manage spatial data, this lecture gives you a good example
  What about images? Videos? Graphs?
You need to understand the concepts introduced
  Spatial data, data types, operations, queries